## Slide 1: GHZ Management SRP Update
Senior Specialist, PI Reliability (Enbridge)
Fall 2025 Meeting
October 22nd 2025
Nader Yoosef-Ghodsi

## Slide 2: Agenda
GHZ Management SRP Overview
Current Roadmap
Status of Key Outcomes
Next Steps for the SRP

## Slide 3: GHZ SRP Overview
Outcomes and Value to Industry
Stakeholders
Industry Improvement
This Strategic Research Priority will result in optimization of the integrity management of hydrotechnical hazards for both natural gas and liquid hydrocarbon pipelines.
Common data dictionary of relevant geomorphological and hydrotechnical terms to enable direct comparison of the data sets collected by different operators through different approaches.
Develop metrics to evaluate effectiveness of mitigation options through comparison of duration of design performance, and life-cycle cost of mitigations.
Develop effective temporary and permanent mitigation options that go beyond armoring and horizontal directional drilling (HDD) of the water crossing.
Develop continuous monitoring techniques of channel scour to enable validation of the hydrological models and cumulative event loading on the pipeline.
Develop geohazard interaction modelling to identify susceptible locations of slope failure following extreme hydrotechnical events.
Geotechnical threats near water crossings following an extreme hydrotechnical event (either precipitation or flood events), and the interaction between the hazards.
Technologies for remote and continuous monitoring of the water crossings and pipeline condition to enable reinstatement of operations after an extreme event.
Effectiveness of the temporary and permanent remediation options at water crossings.
Pipeline Operators
Regulators
Researchers
Industry Service Providers
Pipeline Industry Organization Partners

## Slide 4: Current Roadmap

## Slide 5: Key Outcomes of current projects

## Slide 6: Assessing Interactive Threats at Pipeline Waterway Crossings
ENV-4-1B

## Slide 7: ENV-4-1B – Framework
This project will be multi-phased with the following components:
Work Package 1 – this phase will have desktop and field components and consist of the screening and initial field investigation items of building bank stability assessments at pipeline waterway crossings.
  Task 1 – Desktop Screening and Programmatic Development
  Task 2 – Field Verification and Threat Assessment
Work Package 2 – this phase will utilize the screening and assessment findings of Phase 1 and generate predictive analysis aspects for each location, including appropriate monitoring and mitigation measures.
*Arcadis will work closely with the PRCI Team on sharing of data/information, development, and implementation of Work Package 2

## Slide 8: ENV-4-1B: Interactive Threats
Overview
Status
Active Task(s)
Cost to Date
Status: Critical Needs Attention On Plan
Activities Underway/Completed (since last report)
Continuing Task 2
Overall Project Status/Significant Findings
NA
Current Issues, Risks and Decisions Needed
NA
Planned Activities (next period)
Continue Task 2 efforts
Provide updates at Team and TC meetings
Rationale/Explanation of Deviations between Plan and Forecast
Completed Task 1, and on track with Task 2
Overall Schedule
PM
Task 2
Lump sum billings in September 2024, December 2024, March 2025, April 2025, and July 2025
None currently
Threats/Scope
Changes or Additions

## Slide 9: Screening Assessment
www.prci.org
Based on ENV-4-1A fictious pipeline:
~3,000 miles
~4,500 inventoried waterway crossings
Developed ‘screening’ protocol and worksheet

## Slide 10: Screening Assessment Worksheet
www.prci.org
Screening Based on Visual Assessment Of:
Soil Type
Vegetation Cover
Depressions/Sinkholes
Historical Landslides
Bank Cutting/Erosion
Land Drainage
Drainage Area (Bank Height)
Known hydrotechnical threats

## Slide 11: Soil Type
www.prci.org
Clay soil: 5 (High risk)
Loamy soil: 4 (Moderate risk)
Sandy soil: 3 (Low risk)
Rocky soil: 2 (Very low risk)
Bedrock: 1 (Minimal risk)

## Slide 12: Vegetation Cover
www.prci.org
No vegetation: 5 (High risk)
Sparse vegetation: 4 (Moderate risk)
Moderate vegetation: 3 (Low risk)
Dense vegetation: 2 (Very low risk)
Very dense vegetation: 1 (Minimal risk)
2024
2018
2016

## Slide 13: Depressions/Sinkholes and Historical Landslides
www.prci.org
Depressions/Sinkholes
Many large depressions/sinkholes: 5 (High risk)
Several small depressions/sinkholes: 4 (Moderate risk)
Few small depressions/sinkholes: 3 (Low risk)
Isolated small depressions/sinkholes: 2 (Very low risk)
None: 1 (Minimal risk)
Landslides
Several major landslides: 5 (High risk)
Few major landslides: 4 (Moderate risk)
Several minor landslides: 3 (Low risk)
Few minor landslides: 2 (Very low risk)
No historical landslides: 1 (Minimal risk)

## Slide 14: Bank Cutting/Erosion
www.prci.org
Severe bank cutting: 5 (High risk)
Moderate bank cutting: 4 (Moderate risk)
Minor bank cutting: 3 (Low risk)
Minimal bank cutting: 2 (Very low risk)
No bank cutting: 1 (Minimal risk)

## Slide 15: Land Drainage and Drainage Area (Bank Height)
www.prci.org
Land Drainage
Very poor drainage: 5 (High risk)
Poor drainage: 4 (Moderate risk)
Moderate drainage: 3 (Low risk)
Good drainage: 2 (Very low risk)
Excellent drainage: 1 (Minimal risk)
Drainage Area Correlation
Depth = 0.30DA^0.213
>138,235 sq mi (>15ft): 5 (High risk)
48,460-138,235 sq mi (12-15ft): 4 (Moderate risk)
7,230-48,460 sq mi (8-12ft): 3 (Low risk)
794-7,230 sq mi (5-8ft): 2 (Very low risk)
<795 sq mi (<5ft): 1 (Minimal risk)

## Slide 16: Known Hydrotechnical Threats
www.prci.org
Hydrotechnical Screening Criteria (ENV4-1A)
Scour
Erosion
Avulsion
Interactive Scoring
Geotechnical screening looks at specifically avulsion score and factors in the risk of avulsion occurring into the overall screening

## Slide 17: Screening Assessment Scoring
www.prci.org
Risk Rating Scale:
7-12: Minimal Risk
13-16: Low Risk
17-22: Moderate Risk
23-28: High Risk
29-35: Very High Risk

## Slide 18: Screening Update
www.prci.org

## Slide 19: Task 2 – Field Verification and Threat Assessment
Based on ENV-4-1A fictious pipeline:
~3,000 miles
~4,500 inventoried waterway crossings
The ‘screening’ protocol and worksheets developed in Task 1 were used to select Task 2 sites
Notes: Scope Approach
  ‘Originally’ four locations (selected six) will be selected out of the Task 1 findings (depending on proximity to each other and access considerations)
  Up to two of these six locations will be reinspected based on weather/geologic events
  Collect data on bank conditions (e.g., height, angle, soil characterization) and document signs/features related to bank
  Compile data collected from the field inspections into a database that will be used as the basis for developing a baseline qualitative numeric rating system
  Compare any discrepancy between desktop review and the locations selected for field observations

## Slide 20: Colorado Sites
4 Total Sites
  3 sites had solid correlation with desktop scores
  1 site had a notable difference in bank height score
  Some variation in vegetation score at the time of survey (to be expected)
Lessons Learned/Screening Refinement
  Bank height and land drainage score can vary when there are multiple small waterways in an area
  Additional sources like the USGS National Mapper should be utilized
  If scores reflected the correct bank heights it would have properly classified the crossing

## Slide 21: NY Sites
Chittenango Creek/Oneida Creek
  Screening scores of 16
  Good correlation for most categories
    Soil Type
    Vegetation Cover
    Depressions/sinkholes
    Historical landsides
    Land drainage
    Bank height
Lessons Learned
  Bank undercutting and erosion scores were slightly higher than field conditions
  Overall score was still an accurate range to be placed in

## Slide 22: Site Analysis

## Slide 23: Site Analysis

## Slide 24: Desktop study on effectiveness of hydrotechnical mitigation options
GHZ-03-01

## Slide 25: GHZ-03-01 – Desktop study on effectiveness of hydrotechnical mitigation options
Project Status/Outcomes to Date
Task 1: Literature review of pipeline & similar sector measures (Completed)
Next Steps
Collecting final examples and report drafting
Task 2: Evaluation/analysis. Grouped, drafted guidance table for mitigation selection criteria. (Completed)
Task 3: Case Studies. Operator examples were limited. Expanded to other sectors & white papers. (85% Complete)
Task 4: Draft Final Report started. (due December 2025)
Final Report due April 2026.

## Slide 26: Desktop review and gap analysis of remote and continuous scour monitoring technologies
GHZ-03-02

## Slide 27: GHZ-03-02 – Desktop review and gap analysis of remote and continuous scour monitoring technologies
Project Status/Outcomes to Date
Deliverable 1: Literature review and industry survey on the current state of scour monitoring technologies. (Completed)
Next Steps
Proceed with GHZ-03-04 (Field Testing)
Deliverable 2: Gap analysis. (Completed and Combined with Deliverable 1)
Deliverable 3: Recommended technologies and vendors (as applicable) for field trials in the 2025-2027 timeframe. (Completed)
Deliverable 4: Recommended scope, performance metrics to evaluate the success of the technologies, permitting requirements, and a schedule for the field trials. (Completed)
Deliverable 5: A final report and presentation summarizing the above (Completed)
Webinar held on 7/22/25

## Slide 28: Literature Review – Summary of Findings
Most scour monitoring (pipelines and other industries) is based on predictive modeling and direct physical surveys
  Predictive models are indirect method of evaluating scour based on data such as stream gauges, precipitation, etc.
  Physical surveys measure channel elevation before and after floods
    Generally, do not measure total depth of scour

## Slide 29: Recommended Technologies and Approaches
Deployable: profiling or mapping a streambed and/or pipeline elevation before/after flood events
  In theory, can be used at any crossing
Installed – Riverbed: fixed-location systems that monitor changes in the riverbed associated with scour
  Generally, most effective at smaller streams or intermittent channels where installation would be relatively straightforward
Installed – Pipeline: fixed-location systems that monitor a pipeline to identify potential exposure resulting from scour
  Generally, most effective at larger, perennial river crossings, where conducting riverbed monitoring is impractical due to the difficulty of installing scour monitoring devices

## Slide 30: Deployable
ASV
Autonomous surface vehicles (ASV), to conduct bathymetric surveys during a flood
Uncrewed vessels that can be operated remotely
Used to measure channel profile
Can be combined with pipeline positional surveys (such as from ILI or high-resolution pipeline surveys) to evaluate depth of cover/exposure
Must be manually deployed and require line of sight control

## Slide 31: Deployable
UAS
Unmanned aerial system (UAS) – drones
High-resolution magnetic mapping system using UAS to map pipeline position at river crossings
Can be combined with bathymetry for DOC
Must be manually deployed and require line of sight control

## Slide 32: Installed – Riverbed
Float Out Systems
Buried in the riverbed and when exposed by scour, float to the water surface
May be difficult to install in areas with flowing water (e.g., perennial streams)
May be suitable for intermittent streams with high flow variability

## Slide 33: Installed – Riverbed
Gravity-based devices
Smart rocks or sliding rods/collars
Fall into a scour hole during scour event

## Slide 34: Installed – Riverbed
Sound-Wave Devices
Use sound waves to measure changes in the riverbed elevation
Suitable for testing if structure is available to mount the devices
e.g., sonic fathometers (essentially, fish-finder-type units)
Can be attached to remote monitoring units (RMUs) for near real-time monitoring, and are generally accurate

## Slide 35: Installed – Pipeline
Thermometry Systems
Sensors installed on either side of a watercourse crossing measure the temperature of the pipeline
Detected change in temperature could represent pipeline exposure due to scour
From Ariaratnam and Lich, 2023; image credited to PureHM

## Slide 36: Installed – Pipeline
Fiber Optic
Cable installed inside of pipeline at river crossing, to provide acoustic and strain measurements

## Slide 37: Installed – Pipeline
Acoustic Systems
Placed on the pipeline to monitor acoustical signatures of a real-time scour event
Image from HiFi Brochure

## Slide 38: Testing Locations
21 locations proposed by project team
5 sites selected as primary based on:
  Suitability for multiple testing types
  Ease of access
  Crossing characteristics
    High likelihood of scour
    High predictability of flooding
    High variability of flows
    Low DOC of pipeline
Primary sites:
  Wabash River (Illinois/Indiana)
  Mill Creek (Utah)
  Fish Creek (West Virginia)
  West Fork Grand River (Missouri)
  Nooksack River (Washington)
Notes: Primary = green
Secondary = white
Tertiary = blue

## Slide 39: Fitness-for-service framework to address circumferential cracks near water crossings
GHZ-03-03

## Slide 40: GHZ-3-03 – Project Tasks
Task 1: Kick-Off Meeting
Task 2: Identification of Circumferential Cracks
Task 3: Methodology to Incorporate Concrete Weights
Task 4: Outline Static and Dynamic Loading Scenarios
Task 5: Methods to Estimate Cumulative Damage
Task 6: Update to Fracture Guidelines and Assessment Methods
Task 7: Framework for Stress and Strain-Based Assessment
Task 8: Risk Assessment Framework
Task 9: Integrity Management Recommendations
Task 10: Project Management and Reporting

## Slide 41: GHZ-3-03 Fitness-for-service framework to address circumferential cracks near water crossings
Characteristics | Ls/Lf | Lc/Lf | Dc/Dp
Short Riverweights Closely Spaced | 0.02 | 0.02 | 0.5
Short Riverweights Widely Spaced | 0.15 | 0.02 | 0.5
Long Riverweights Closely Spaced | 0.02 | 0.2 | 0.5
Long Riverweights Widely Spaced | 0.15 | 0.2 | 0.5
Outcomes to Date
Task 2 and 3 has been initiated
Literature review is ongoing for Task 2: Identification of circumferential cracks
Numerical analysis is ongoing (Task 3).
The effects of concrete river weights on VIV of an exposed pipe in a river crossing is incorporated by:
Conducting a detailed Fluid Structure Interaction Analysis (Combining CFD and FEA)
A numerical experiment has been designed to conduct a parametric study
Introduction of non-dimensional parameters (as shown in the table) to characterize the physical dimensions and characteristics of concrete and pipe
Updating (with a correction factor) the existing response model of DNV-RP-F105 based on the findings of parametric study

## Slide 42: GHZ-3-03 Fitness-for-service framework to address circumferential cracks near water crossings
In-Line Displacement
Crossflow Displacement
CFD simulation of a plain pipe
FSI Result of first case in the parametric study (with concrete weights, Short Riverweights Closely Spaced)
Outcomes to Date
Following are the updates so far on Task 3
Conducted preliminary studies that includes
Grid Convergence Study
Temporal Convergence Study
Pre-processing of first set of parameters (9 cases)
CAD and Mesh generation
Initialization of FSI cases with transient CFD analysis on a stationary pipe with concrete coatings
FSI analysis of these cases are currently in progress (4 cases out of 36 cases are completed so far).

## Slide 43: GHZ-3-03 Fitness-for-service framework to address circumferential cracks near water crossings
Continue the pre-processing of remaining set of parametric study cases
Next Steps
While Running the FSI analysis cases simultaneously
Post-processing of the results for first set of analysis case
Continue to make progress on remaining tasks
Expected completion time: August 2026

## Slide 44: Field Validation of Remote and Continuous Scour Technologies
GHZ-03-04

## Slide 45: GHZ-03-04 – Field Validation of Remote and Continuous Scour Technologies
Project Status/Outcomes to Date
Bids for primary contractor received 09/15/2025
Primary contractor has been selected and is being onboarded.
Next Steps
Complete onboarding of primary contractor.
Begin natural resource/environmental permitting efforts at field sites.
5 primary sites and 3 backup sites
Work with Operators to coordinate installation and deployment of technologies at each primary site.
Collect and analyze scour data over the life of the project.
Compare technology performance and scour predictions based on performance indicators set by the project team.

## Slide 46: GHZ-03-04 – Field Validation of Remote and Continuous Scour Technologies
Timeline
  Mid-late 2025
    Onboard contractors and begin permitting efforts.
  2026
    Complete permitting of sites.
    Install and deploy scour technologies
    Begin data collection.
  2027+
    Collect and analyze scour data
    Maintain instrumentation as needed.
  2029
    Perform technology comparison based on collected data.
    Generate final report assuming notable scour events occurred within the project timeframe.

## Slide 47: Next Steps for the SRP

## Slide 48: Preparation for 2026