## Slide 1: R&D-Based Decision Optimizer
Executive Assembly Meeting
Executive Director, Knowledge Transfer
Oct 22, 2025
Shahani Kariyawasam, Ph.D., P.Eng.
Nashville
Notes: Story –
At REX 2025 at the Panel on AI – Michael Bellamy – presented some great R&D work Baker Hughes had performed using ML to specify ILI error in a defect specific manner – This was done 6 to 8 years ago. His main concern was that the R&D was done the technology was available for use, it reduced a significant number of digs (bringing great value) yet Adoption by industry was very poor! So he asked why ? Why are we not adopting valuable available R&D?
This is not an isolated case. Psqr model is another example.
We did go on to discuss how many operators;
1) firstly, do not have the decision framework/process/software to receive new technologies/methods/models - defect specific ILI error, Psqr cannot be readily adopted by many fitness for service processes or software.
2) The secondary reason is that many decision makers do not have a clear view of cost benefit – Is the effort and resources needed to implement the new technology worth the returns in value – in the reduction of digs?
3) Most operators do not have the people to build the required framework and communicate the cost benefit
This is the need we are trying to satisfy !

## Slide 2
Effect of R&D
Improve Input with better technologies (E.g., high resolution vs low resolution ILI)
Continuously improve engineering models, technologies, and processes (E.g., ILI error representation, corrosion growth process, assessment model, etc)
Ensure safety and reduce unnecessary actions, resource allocation - $$, time (E.g., number of digs, number of failures)
Input Data
Engineering Models
Technologies
Processes
Integrity Decisions ($$, Resources)
Value of R&D in Safety Decisions
© 2025, Pipeline Research Council International
Notes: Operators take - Many safety related technical decisions. Input data – that is processed using Eng Models, technologies, processes that lead to integrity decisions which cost operators $$ and resources.
R&D can improve the input data ( like using hires instead of low res ILI data) and ………..
One of the high budget critical decisions particularly for vintage pipelines is corrosion and crack ILI based dig decisions

## Slide 3: Why are Valuable Improvements Not Always Adopted?
Issues | Solution
R&D address components of the decision-making system. Operators lack Systems/Framework to receive R&D. | Build flexible API based software system to integrate many subsystems and gain system reliability.
The benefit to the company (or engineer/leader) is not always clear | Software built to clearly communicate benefits with examples and refs
Operators are busy with operational demands- lack time to implement systems | Enable easy transparent implementation and upgrades
Not comfortable (and all may not have the expertise) with defending change to regulators or leaders | Provide basis for R&D, clear communication system, wide adoption and related PRCI documentation and support.
Notes: another problem is that we don’t approach our R&D cohesively with a plan to have the results added to a decision tool. FFS tools are ad-hoc and commonly employ different research contractors who pick the software of their choice, sometimes not even producing a usable tool, just demonstrating the capabilities in modeling tools (e.g., Mathcad, Excel).

## Slide 4: Corrosion (& Cracking) and Post ILI Failure Trends
Ref: Huang, T. and Kariyawasam, S. 2018. An ILI Based Program That Prevents Reoccurrence of Post ILI Failures Seen in Industry. Proceedings of the 2018 12th International Pipeline Conference, IPC2018-78604

## Slide 5: Real Example – Effect of Sharper Tools on Number of Digs

## Slide 6
Year 0, FPRRSTRENG distribution
Example : 2017 ILI – Focus on Rupture Threat
© 2025, Pipeline Research Council International

## Slide 7
R&D
PIT specific growth
Cluster specific growth
Growth Granularity
R&D
Signal-to-signal
run comparison
No run comparison
Growth Magnitude
R&D
Deterministic 1.25
Probabilistic 1E-3
Uncertainty
R&D
Deterministic, add 10% & 10 mm
Probabilistic, ± 10 %WT (10mm), 80% time
Deterministic, add 20% & 20 mm
Probabilistic, ± 20 %WT (20mm), 80% time
ILI Measurement Error
R&D
PIT – MB31G
Cluster – RSTRENG
B31G
MB31G
PIT – MB31G
& Cluster - Psqr
Assessment Model
Method | Threshold | Depth Error | Length Error | Model | Growth Rate |  | # Excavations in year |  |  |  |  |  |  | # reported features
 |  |  |  |  |  |  | 0 | 1 | 2 | 3 | 4 | 5 | 0~5 sum | 
Deterministic | 1.25 | Add 10% WT to depth |  | PIT MB31G Cluster RSTRENG | RunCom | Cluster-specific | 149 | 30 | 42 | 30 | 40 | 46 | 337 | 182619
 |  | Add 10% WT to depth & 10 mm to length |  |  |  |  | 169 | 34 | 29 | 37 | 54 | 53 | 376 | 
Probabilistic | 1E-03 | +/-10 %WT (10mm), 80% time |  |  |  |  | 1 | 19 | 21 | 40 | 38 | 61 | 180 | 
Decision Comparison – Deterministic vs Probabilistic
© 2025, Pipeline Research Council International

## Slide 8
R&D
PIT specific growth
Cluster specific growth
Growth Granularity
R&D
Signal-to-signal
run comparison
No run comparison
Growth Magnitude
R&D
Deterministic 1.25
Probabilistic 1E-3
Uncertainty
R&D
Deterministic, add 10% & 10 mm
Probabilistic, ± 10 %WT (10mm), 80% time
Deterministic, add 20% & 20 mm
Probabilistic, ± 20 %WT (20mm), 80% time
ILI Measurement Error
R&D
PIT – MB31G
Cluster – RSTRENG
B31G
MB31G
PIT – MB31G
& Cluster - Psqr
Assessment Model
Method | Threshold | Depth Error | Length Error | Model | Growth Rate |  | # Excavations in year |  |  |  |  |  |  | # reported features
 |  |  |  |  |  |  | 0 | 1 | 2 | 3 | 4 | 5 | 0~5 sum | 
Probabilistic | 1E-03 | +/-10 %WT (10mm), 80% time |  | PIT MB31G Cluster RSTRENG | RunCom | Cluster-specific | 1 | 19 | 21 | 40 | 38 | 61 | 180 | 182619
 |  | +/-20 %WT (20mm), 80% time |  |  |  |  | 1 | 430 | 154 | 246 | 273 | 409 | 1513 | 
Decision Comparison – ± 10 %WT vs ± 20 %WT
© 2025, Pipeline Research Council International

## Slide 9
R&D
PIT specific growth
Cluster specific growth
Growth Granularity
R&D
Signal-to-signal
run comparison
No run comparison
Growth Magnitude
R&D
Deterministic 1.25
Probabilistic 1E-3
Uncertainty
R&D
Deterministic, add 10% & 10 mm
Probabilistic, ± 10 %WT (10mm), 80% time
Deterministic, add 20% & 20 mm
Probabilistic, ± 20 %WT (20mm), 80% time
ILI Measurement Error
R&D
PIT – MB31G
Cluster – RSTRENG
B31G
MB31G
PIT – MB31G
& Cluster - Psqr
Assessment Model
Method | Threshold | Depth Error | Length Error | Model | Growth Rate |  | Critical features needed to be excavated in year |  |  |  |  |  |  | # reported features
 |  |  |  |  |  |  | 0 | 1 | 2 | 3 | 4 | 5 | 0~5 sum | 
Probabilistic | 1E-03 | +/-10 %WT (10mm), 80% time |  | PIT MB31G Cluster RSTRENG | RunCom | Cluster-specific | 1 | 19 | 21 | 40 | 38 | 61 | 180 | 182619
 |  |  |  |  | NO RunCom |  | 1 | 59 | 23 | 43 | 59 | 70 | 255 | 
Decision Comparison – RunCom vs No RunCom
© 2025, Pipeline Research Council International

## Slide 10
R&D
PIT specific growth
Cluster specific growth
Growth Granularity
R&D
Signal-to-signal
run comparison
No run comparison
Growth Magnitude
R&D
Deterministic 1.25
Probabilistic 1E-3
Uncertainty
R&D
Deterministic, add 10% & 10 mm
Probabilistic, ± 10 %WT (10mm), 80% time
Deterministic, add 20% & 20 mm
Probabilistic, ± 20 %WT (20mm), 80% time
ILI Measurement Error
R&D
PIT – MB31G
Cluster – RSTRENG
B31G
MB31G
PIT – MB31G
& Cluster - Psqr
Assessment Model
Method | Threshold | Depth Error | Length Error | Model | Growth Rate |  | Critical features needed to be excavated in year |  |  |  |  |  |  | # reported features
 |  |  |  |  |  |  | 0 | 1 | 2 | 3 | 4 | 5 | 0~5 sum | 
Probabilistic | 1E-03 | +/-10 %WT (10mm), 80% time |  | PIT MB31G Cluster RSTRENG | RunCom | Cluster-specific | 1 | 19 | 21 | 40 | 38 | 61 | 180 | 182619
 |  |  |  | PIT MB31G Cluster Psqr |  |  | 0 | 0 | 0 | 0 | 0 | 4 | 4 | 
Decision Comparison – RSTRENG vs Psqr
© 2025, Pipeline Research Council International

## Slide 11
R&D
PIT specific growth
Cluster specific growth
Growth Granularity
R&D
Signal-to-signal
run comparison
No run comparison
Growth Magnitude
R&D
Deterministic 1.25
Probabilistic 1E-3
Uncertainty
R&D
Deterministic, add 10% & 10 mm
Probabilistic, ± 10 %WT (10mm), 80% time
Deterministic, add 20% & 20 mm
Probabilistic, ± 20 %WT (20mm), 80% time
ILI Measurement Error
R&D
PIT – MB31G
Cluster – RSTRENG
B31G
MB31G
PIT – MB31G
& Cluster - Psqr
Assessment Model
Method | Threshold | Depth Error | Length Error | Model | Growth Rate |  | Critical features needed to be excavated in year |  |  |  |  |  |  | # reported features
 |  |  |  |  |  |  | 0 | 1 | 2 | 3 | 4 | 5 | 0~5 sum | 
Probabilistic | 1E-03 | +/-10 %WT (10mm), 80% time |  | PIT MB31G Cluster Psqr | RunCom | Cluster-specific | 0 | 0 | 0 | 0 | 0 | 4 | 4 | 182619
 |  |  |  |  |  | PIT- specific | 0 | 0 | 0 | 0 | 0 | 2 | 2 | 
Decision Comparison – PIT-specific vs Cluster-specific growth
© 2025, Pipeline Research Council International

## Slide 12
This same ILI run program based on inputs and sub-processes can safely give you anywhere from 2 to 1513 digs
Most commonly, sharper tools reduce large numbers of unnecessary digs however they may add a few more necessary digs
More precise methods (through R&D and improvement) give higher safety and economy – optimizing resources
Value of improvement can be demonstrated – to leadership and regulators
The Example Demonstrates
© 2025, Pipeline Research Council International
AXE

## Slide 13
Smarter Tools
With Data
Worst case
Without Data
Performance
Economy
Max
Max
Why Sharper Tools Bring Performance and Economy
© 2025, Pipeline Research Council International

## Slide 14: Corrosion Post ILI Failure Trends
Ref: Huang, T. and Kariyawasam, S. 2018. An ILI Based Program That Prevents Reoccurrence of Post ILI Failures Seen in Industry. Proceedings of the 2018 12th International Pipeline Conference, IPC2018-78604

## Slide 15: Moving from Components to System Reliability
Safety related decisions are made using many inputs & sub-processes (components).
Pipeline industry has developed these component improvements, which have been available for many years and decades.
Many operators use some of these component processes. But few use all system optimized combinations (from 1513 to 2 digs as appropriate) with consistent system reliability.
Other high reliability industries use system reliability methods which enable the full use of AI and data capability
A system is only as
strong as the weakest link
System optimization gives optimized
performance and economy
Consistent
system
reliability

## Slide 16: Discussion
Many operators lack a framework/system in which to implement the R&D improvements and the tools to understand impact and defend to leaders/regulators.
Start with Corrosion Management System in 2026 (Cracks & Dents 2027-2028)
PRCI R&D-based Decision Optimizer will provide (Idea 5003):
  Analytical Software that compares R&D improvements to make optimum decision:
    Develops this System that is modular, able to adopt new models and AI+data driven processes
    Continuously updates the R&D results – as a simple to use tool
    Provides the many optional paths an operator can take (based on circumstances and need)
  Clear communication and defendable examples to demonstrate safety and value – with industry database for sandbox of ROI examples
  Plan to leverage existing software development expertise and modules for timely deliverables
Timely - Accelerated AI capability, Regulatory environment in US.

## Slide 18
Moving Forward
© 2025, Pipeline Research Council International
R&D-based Decision Optimizer (RDO) is a systems approach to ensure components are integrated via data driven acceptable reliability levels and related optimized decisions for any safety-based decision process.
This will enable component research like ILI improvements to adopt AI and data driven improvements
First implementation - ILI based dig programs drive high budget & can give the highest value to members – Corrosion and Cracks then others
Timely - Regulatory environment in US, etc. Accelerated AI capability.
Notes: Regulatory environment is right
Baker Hughes

## Slide 19: Backup

## Slide 20: Call to Action
Developing business model
Initiating project in Q4 2025 – funding portal
Great support from industry leaders
Join the team to incorporate your needs and receive a tool that enables your leadership in 21 Century!

## Slide 21: Purpose of this Presentation
High Value Initiative
Based on REX panel and other discussions
Growth in member support
Timely - regulatory environment, AI and data driven work
Opportunity to join team